reprapltd.com

        e-mail: contact@reprapltd.com
        tel: 01249 740621

Manufacture and testing of small solid-fuel rocket engines

Buildings Schedule

See the attached site layout.

Our buildings consist of three laboratories of about 4m x 4m, an office of the same size, an entrance foyer, and a larger lab about 3m x 12m. The building is made from concrete blocks and brickwork, and has a thermally-insulated steel roof. It is always locked when unattended.

The central laboratory is our chemistry lab, and it is there that the components of the solid rocket fuel that we wish to use for testing will be stored. Two of the three components are non-hazardous: aluminium powder and butyl rubber. These will be stored with other chemical reagents. (Note: aluminium powder is dangerous as a dust suspension in the air; precautions will be taken against that.)

The third fuel component is the oxidising agent ammonium perchlorate. This will be stored separately from all other materials in the chemistry laboratory in a locked steel cabinet.

The total quantity of all three components stored will be less than 2Kg.

No mixed rocket fuel will be stored; it will be manufactured in small quantities (< 100g) as required.