reprapltd.com

HM Explosives Inspectorate	16 April 2018
Health & Safety Executive
5S.2	e-mail: contact@reprapltd.com
Redgrave Court	tel: 01249 740621
Merton Road
Bootle
Merseyside
L20 7HS

Dear Sir or Madam,

Manufacture and testing of small solid-fuel rocket engines

I enclose, completed, form LP41 to apply for an explosives licence for this company. I also enclose a building schedule for this site, and scaled plans showing the site location and its surroundings and the site layout. The appropriate fee would seem to be that for “Licence to manufacture explosives by means of on-site mixing”, for which I enclose a cheque for £243.00.

We have invented a new type of solid-fuel rocket motor, and we wish to test it before we look to licence the technology (if it works) in the aerospace industry. Solid fuel motors have the advantage of stable fuel storage and quite high specific impulse. But conventional designs lack the ability to be shut-down and restarted under control. Our new motor should have that ability.

We intend to manufacture small-scale engines (largest dimension less than 100mm) for testing, and small quantities of propellant (less than 100g per batch) to facilitate those tests. We shall only be doing outdoor bench testing, and shall not be launching or doing flight tests. We cannot buy standard solid propellant from other manufacturers because we need it formed with a novel geometry for our new engine. Thus we must manufacture it ourselves.

We shall not be storing any mixed propellant; we shall make it as required. And we shall only be storing small quantities of the components (less than 2Kg in total) as separated raw materials. Those components are aluminium powder, ammonium perchlorate, and butyl rubber.

If you have any questions, please don't hesitate to contact me.

Yours faithfully

Dr Adrian Bowyer
Director	encs.